Specify Lyon

Lyon LLC	July 2012

PO Box 671

Aurora, Illinois  60507

Toll Free	(800) 323-0082

Phone	(630) 892-8941

Fax	(800) 367-6681

Web Site	www.lyonworkspace.com

E-Mail	lyon@lyonworkspace.com

Product Guide Specification

Specifier Notes:  This product guide specification is written according to the Construction Specifications Institute (CSI) 3-Part Format, including MasterFormat, SectionFormat, and PageFormat, as described in The Project Resource Manual—CSI Manual of Practice, Fifth Edition.

The section must be carefully reviewed and edited by the Architect to meet the requirements of the project and local building code.  Coordinate this section with other specification sections and the Drawings.  Delete all “Specifier Notes” after editing this section.

Section numbers are from MasterFormat 1995 Edition, with numbers from MasterFormat 2004 Edition in parentheses.  Delete version not required.

SECTION 10501 (10 51 13)

STANDARD STEEL LOCKERS

Specifier Notes:  This section covers Lyon LLC standard steel lockers.  Consult Lyon LLC for assistance in editing this section for the specific application.

PART 1	GENERAL

1.1	SECTION INCLUDES

A.	Standard steel lockers.

1.2	RELATED SECTIONS

Specifier Notes:  Edit the following list of related sections as required for the project.  List other sections with work directly related to the lockers.

A.	Section 03300 (03 30 00) – Cast-in-Place Concrete:  Concrete bases.

B.	Section 06100 (06 10 00) – Rough Carpentry:  Wood ground and furring for anchoring lockers.

C.	Section 09650 (09 65 13.13) – Resilient Base.

1.3	REFERENCES

Specifier Notes:  List standards referenced in this section, complete with designations and titles.  This article does not require compliance with standards, but is merely a listing of those used.

A.	ASTM A 653 – Standard Specification for Steel Sheet, Zinc-Coated (Galvanized) or Zinc-Iron Alloy-Coated (Galvannealed) by the Hot-Dip Process.

B.	ASTM A 1008 – Standard Specification for Steel, Sheet, Cold-Rolled, Carbon, Structural, High-Strength Low-Alloy and High-Strength Low-Alloy with Improved Formability.

1.4	SUBMITTALS

A.	Comply with Section 01330 (01 33 00) – Submittal Procedures.

B.	Product Data:  Submit manufacturer's product data and installation instructions.

Specifier Notes:  Delete locker benches from the following paragraph if they are not specified.

C.	Shop Drawings:  Submit manufacturer's shop drawings, indicating construction, materials, dimensions, door frames, doors, handles, locks, ventilation, options, accessories, [locker benches,] finish, locker layout, anchoring, and installation details.

D.	Samples:  Submit manufacturer's standard color samples.

E.	Warranty:  Submit manufacturer's standard warranty.

1.5	QUALITY ASSURANCE

Specifier Notes:  Describe requirements for a meeting to coordinate the installation of the lockers and to sequence related work.  Delete the following paragraph if not required.

A.	Pre-installation Meeting:  Convene pre-installation meeting [2 weeks] [ __________ ] before start of installation of lockers.  Require attendance of parties directly affecting work of this section, including Contractor, Architect, installer, and manufacturer's representative.  Review installation, adjusting, cleaning, protection, and coordination with other work.

1.6	DELIVERY, STORAGE, AND HANDLING

A.	Delivery:  Deliver materials to site in manufacturer's original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

B.	Storage:  Store materials in clean, dry area indoors in accordance with manufacturer's instructions.

C.	Handling:  Protect materials and finish during handling and installation to prevent damage.

PART 2	PRODUCTS

2.1	MANUFACTURER

A.	Lyon LLC, PO Box 671, Aurora, Illinois 60507.  Toll Free (800) 323-0082.  Phone (630) 892-8941.  Fax (800) 367-6681.  Web Site www.lyonworkspace.com.  E-Mail lyon@lyonworkspace.com.

2.2	STANDARD STEEL LOCKERS

A.	Model:  Standard Quiet Lockers.

Specifier Notes:  Specify style of lockers.  Multiple-tier lockers are four, five, and six-tiers high.

B.	Style:  [Single tier]  [Double tier]  [Triple tier]  [Four tier]  [Five tier]  [Six tier]  [As indicated on the Drawings].

Specifier Notes:  Specify size of lockers per opening.

C.	Locker Size:  [ _______ inches wide by _______ inches deep by _______ inches high per opening]  [As indicated on the Drawings].

Specifier Notes:  Specify configuration of lockers.

D.	Locker Configuration:  [Single row]  [Double row]  [As indicated on the Drawings].

Specifier Notes:  Specify knocked-down or fully assembled construction.  Knocked-down construction is standard.

E.	Construction:  [Knocked down]  [Fully assembled].

Specifier Notes:  ASTM A 1008 steel is standard.  Specify ASTM A 653 galvannealed steel for high humidity or corrosive atmospheres.

F.	Material:

1.	Steel:  [ASTM A 1008, Class I, mild-annealed, cold-rolled steel, free from surface imperfections]  [ASTM A 653, galvannealed steel].

2.	Bolts:  Zinc plated or other comparable rust-retardant treatment.

G.	Body:

1.	24-gauge steel.

2.	Flanged to give double thickness of metal at back vertical corners.

H.	Door Frame:

1.	16-gauge formed-steel channels.

2.	Vertical Members:  Additional flange to form continuous door strike.

3.	Corners:  Lapped and welded into rigid assembly.

4.	Bottom Cross Members:  Tang at each end that fits through slot in rear flange of upright frame member to prevent twisting out of alignment.

5.	Top and Bottom Cross Members:  Provide support for front edge of locker top and bottom.

I.	Doors:

Specifier Notes:  Specify gauge of doors.  16-gauge is standard.

1.	1-piece, [16-gauge]  [14-gauge] steel.

2.	Single, Double, and Triple-Tier Locker Doors:  Both vertical edges formed into channel-shaped formation.  Top and bottom flanged at 90-degree angle.

3.	Multiple-Tier Locker Doors:  Hinge side formed into channel-shaped formation with other 3 sides flanged at 90-degree angle.

4.	Multiple-Tier Locker Doors, Up to and Including 15 Inches Wide by 15 Inches High:  18-gauge steel, unless otherwise indicated.

J.	Ventilation:

1.	Single-Tier Lockers:

a.	9 Inches Wide:  Six 3-1/2-inch louvers top and bottom.

b.	Over 9 Inches Wide:  Six 6-inch louvers top and bottom.

2.	Double-Tier Lockers:

a.	9 Inches Wide:  Six 3-1/2-inch louvers top and bottom.

b.	Over 9 Inches Wide:  Six 6-inch louvers top and bottom.

3.	Triple-Tier Lockers:

a.	9 Inches Wide:  Two 3-1/2-inch louvers top and bottom.

b.	Over 9 Inches Wide:  Two 6-inch louvers top and bottom.

4.	Multiple-Tier Lockers:

a.	12 Inches and 15 Inches Wide:  Three 3-1/2-inch louvers per door.

b.	18 Inches Wide and Over:  Four 6-inch louvers per door.

Specifier Notes:  The following four sentences specify optional louver arrangements.  Delete if not required.  If any of the optional louver arrangements are specified, delete the appropriate sentence above.

5.	Single-Tier Lockers:  [No louvers]  [Fully louvered]  [Mini louvers].

6.	Double-Tier Lockers:  [No louvers]  [Fully louvered]  [Mini louvers].

7.	Triple-Tier Lockers:  [No louvers]  [Fully louvered]  [Mini louvers].

8.	Multiple-Tier Lockers:  [No louvers]  [Fully louvered]  [Mini louvers].

Specifier Notes:  The following two sentences specify optional diamond-shaped perforations instead of louvers.  Delete if not required.  Perforated sides, backs, tops, bottoms, and intermediate bottoms are also available.  Consult Lyon for additional information.

If the optional diamond-shaped perforations are specified, delete the appropriate sentences above.

9.	Single, Double, and Triple-Tier Lockers:  2 groups of diamond-shaped perforations for each door.

10.	Multiple-Tier Lockers:  1 group of diamond-shaped perforations for each door.

K.	Hinges:

1.	Height:  Minimum of 2 inches.

2.	Type:  0.050-inch thick steel, 5-knuckle, full-loop hinge forming double thickness on each leaf.

3.	Attachment:  Set hinges in slot in door and frame and projection welded to frame and securely attached to door.

4.	Hinge Pin:  Spun over at ends to resist removal.

5.	Single-Tier Lockers, 48 Inches and Higher:  3 hinges.

6.	All Other Tiers:  2 hinges.

7.	Mounting:  Right-hand side of door.

L.	Multi-Point Locking Device:

1.	Single-Tier Lockers, 48 Inches and Higher, Locking Device:  Engage frame at 3 points.

2.	Double and Triple-Tier Locking Device:  Engage frame at 2 points.

3.	Channel-Shaped Locking Device:

a.	Full-length reinforcing ribs.

b.	Quiet design using nylon-guide inserts to reduce metal-to-metal contact.

4.      Lock Bar:  Enclosed on 3 sides and operate within channel formation of door.

5.	Locking Device:  Prelocking so mechanism can be locked in open position.  Door locking automatically when closed.

6.	Door Jambs:

a.	Single-Tier Lockers, 48 Inches and Higher:  3 door jambs.

b.	Double and Triple-Tier Lockers:  2 jambs welded to side of door frames to engage locking device.

c.	Safety Reverse Nose for Each Jamb:  Eliminate hazard of sharp-pointed edges protruding into locker.

d.	Easily replaceable soft rubber bumper for each jamb.

7.	Multiple-Tier Lockers:  14-gauge steel lock clip for attaching padlock.

Specifier Notes:  Single-point latches replace the multi-point locking device and are optional.  Delete if not required.  They are not available on 9-inch wide lockers.  Delete the above sentences if single-point latch is specified.

8.	Single-point latch.

9.	Doors:  Provided with lock hole filler to permit use of built-in key or combination lock.

M.	Handles:

Specifier Notes:  Specify tamper-guard handles, recessed handles, or single-point latching system for single, double, and triple-tier lockers.

Tamper-guard handles are standard.  Used with built-in key locks, combination locks, or coin-deposit lockers.  For use with multi-point locking device only.

1.	Tamper-Guard Handles:

a.	Single, double, and triple-tier lockers.

b.	Chrome-plated, die-cast zinc alloy, with minimum tensile strength of 40,000 psi.

c.	No moving parts shall operate against outside surface of locker.

d.	Padlock Attachment:  Integral part of lift, attached directly to locking bar and protected by fixed-handle housing.

e.	Built-in padlock strike.

Specifier Notes:  Recessed handles are optional on single, double, and triple-tier lockers and 2-person lockers.  Used with built-in key locks, combination locks, or coin-deposit lockers.  For use with multi-point locking device only.  Delete if not required.

2.	Recessed Handles:

a.	Single, double, and triple-tier lockers and 2-person lockers.

b.	4-1/8 inches wide by 6-1/16 inches high by 1-1/4 inches deep.

c.		Flush-front appearance.

d.	Finger lift activates door lock.

Specifier Notes:  Single-point latching system is optional on single, double, triple, and multiple-tier lockers.  Not available on 9-inch wide lockers.  Delete if not required.

3.	Single-Point Latching System:

a.	Single, double, triple, and multiple-tier lockers.

b.	4-1/8 inches wide by 6-1/16 inches high by 1-1/4 inches deep.

c.		Flush-front appearance.

d.	Operates with no moving parts.

e.	Pan reinforcements, 18 gauge.

Specifier Notes:  Specify door pulls for multiple-tier lockers.  Roll-point catch is optional.

4.	Door Pulls:

a.	Multiple-tier lockers.

b.	16-gauge steel door pull with padlock attachment, when not used with built-in locks.

c.	Roll-point catch.

N.	Shelves:

1.	Single-tier lockers.

2.	1 shelf, approximately 9 inches below top.

3.	Single sheet, 24-gauge steel.

4.	Flanged on 4 sides.

5.	Safety Front Flange:  Double flanged with second bend turned 45 degrees.

6.	Attachment:  Minimum of 2 points through each side flange.

O.	Coat Hooks:

1.	Single, double, and triple-tier lockers.

2.	1 double-prong ceiling hook and 3 single-prong wall hooks.

3.	Steel rod stock with ball points for snag-free use.

4.	Attachment:  2 bolts.

5.	Finish:  Zinc-plated or comparable rust-retardant treatment.

P.	Coat Rods:

1.	Use in 18-inch and deeper, knocked-down, single-tier lockers, replacing double-prong ceiling hook.

2.	5/8-inch diameter, galvanized steel.

3.	Attachment:  Bracket with 2 bolts at each end.

Specifier Notes:  Include the following paragraph if free-standing lockers are required.  Front and end closed bases are optional.

Q.	Free-Standing Lockers:

1.	6-inch legs.

2.	Front and end closed bases.

2.3	ACCESSORIES

Specifier Notes:  Specify accessories required and delete the others.  Consult Lyon for assistance in specifying accessories for the specific application.

A.	Extra Shelves:

1.	Single sheet, 24-gauge steel.

2.	Flanged on 4 sides.

3.	Safety Front Flange:  Double flanged with second bend turned 45 degrees.

4.	Attachment:  Minimum of 2 points through each side flange.

Specifier Notes:  Number plates are optional.  Delete if not required.

B.	Number Plates:

1.	Aluminum.

2.	Size:  2-3/4 inches wide by 1 inch high.

3.	Numbers:  Clearly etched numbers a minimum of 3/8 inch high.

4.	Attachment:  Attach in prepunched holes near top of doors.

Specifier Notes:  Specify type of locks.  Lock options can be used with standard locker handle and retrofitted to existing installations.  Consult Lyon for assistance in specifying locks for the specific application.

C.	Locks:  [Built-in combination]  [Built-in key control]  [Combination padlock]  [Key control padlock]  [Safe-O-Mat]  [None].

Specifier Notes:  Specify tops of lockers.  Delete tops not required.  Continuous-sloping hoods mount on one or more standard flat-top lockers.  Individual-sloping tops are furnished on lockers with full-height side panels and backs.

D.	Tops:  [Flat]  [Continuous-sloping hoods]  [Individual-sloping tops].

Specifier Notes:  Specify optional material for bottom of lockers.  Delete if not required.

E.	Bottoms:  [Painted steel, 16 gauge]  [Painted galvannealed steel, 24 gauge]  [Painted galvannealed steel, 16 gauge]  [Unpainted stainless steel, 16 gauge]  [Beige-colored plastic].

Specifier Notes:  Specify bases.  Delete bases not required.

F.	Bases:  [Kitchen cabinet style, 4 inches high, for no-leg lockers]  [Closed style, fit in 6-inch high spaces between legs, for 6-inch leg lockers]  [Z-type, 14-gauge steel, 4 inches high, for no-leg lockers]  [None].

G.	Floor Anchoring:  Anchor lockers to floor in accordance with manufacturer's instructions.

H.	Closures and Fillers:

1.	Top closures, closure strips, front expansion fillers, and corner fillers.

2.	Fill spaces between 2 lockers or between lockers and walls as required for proper fit.

I.	End Panels:

1.	End Cover Panels:  14-gauge steel, construction bolt heads exposed at perimeter.

2.	End Finishing Panels:  16-gauge steel, no bolt heads exposed.

J.	Recess Trim:

1.	End and Top Recess Trim for Lockers to be Placed in Wall Recesses:  18-gauge formed steel with 2-3/4-inch wide face.  Bolted to locker frames.

2.	Top Recess Trim:  Approximately 5'-0" lengths with formed splice cap to cover joints and to hold top recess trim in alignment.

3.	End Recess Trim:  2-3/4 inches higher than lockers and lap over ends of top recess trim for neat joint at top of corners.

Specifier Notes:  Delete the following article if locker benches are not required.

2.4	LOCKER BENCHES

Specifier Notes:  Specify laminated hardwood, plastic laminate, or anodized aluminum locker benches.  Consult Lyon for assistance in specifying locker benches for the specific application.

A.	Laminated Hardwood Benches:

1.	Top:  Laminated hardwood with clear coat finish.

Specifier Notes:  Specify length of top.  Length ranges from 3 to 12 feet in 1-foot increments.

a.	Size:  9-1/2 inches wide by 1-1/4 inches thick by _______ feet long.

b.	Finish:  Acrylic, 2 coats.

Specifier Notes:  Specify pedestals.  Enameled steel is standard.

2.	Pedestals:  [14-gauge enameled steel with 1-5/8-inch tubing uprights]  [Heavy-duty enameled cast iron]  [Anodized aluminum extrusion, Type 6105-T5, 2 pieces, 2-1/4 inches by 3/4 inch, formed and unit welded].

Specifier Notes:  Pedestal finish is for enameled steel and cast iron.

a.	Finish:  Same color as lockers.

B.	Plastic Laminate Benches:

1.	Top:  [Color matched]  [Wood laminated].

a.	Core:  Laminated hardwood.

b.	Long Sides:  Full 180-degree soft edge.

Specifier Notes:  Specify length of top.  Length ranges from 3 to 12 feet in 1-foot increments.

c.	Size:  12 inches wide by 1-3/4 inches thick by  _______ feet long.

Specifier Notes:  Specify pedestals.  Enameled steel is standard.

2.	Pedestals:  [14-gauge enameled steel with 1-5/8-inch tubing uprights]  [Heavy-duty enameled cast iron].

a.	Finish:  Same color as lockers.

C.	Anodized Aluminum Benches:

Specifier Notes:  Specify bench type.

1.	Type:  [Portable]  [Fixed-position].

Specifier Notes:  Specify length of top.  Length ranges from 3 to 12 feet in 1-foot increments.

2.	Top:  9-1/2 inches wide by _______ feet long.

3.	Pedestals:  Anodized aluminum extrusion, Type 6105-T5, 2 pieces, 2-1/4 inches by 3/4 inch, formed and unit welded.

4.	Base:  12-5/8 inches wide by 14-5/8 inches high.

D.	Pedestals:

1.	Spacing:  Maximum of 6-foot centers.

2.	Overall Height:  17-3/4 inches.

3.	Attachment:  Attach to top with 2 lag screws.  Anchor to floor with 4 suitable anchors.

2.5	FINISH

A.	General:  Factory apply finish in accordance with manufacturer's instructions.

B.	Standard Finish: Exposed steel parts shall be thoroughly cleaned, given bonding and rust-inhibitive phosphate treatment, and electrostatically sprayed with powder coat.  Baked-on finish.

Specifier Notes:  An optional antimicrobial finish is available on all Lyon lockers.  Delete if not required.  Consult Lyon for additional information.

C.	Antimicrobial Finish:  Apply antimicrobial finish.

D.	Color:

Specifier Notes:  Specify exterior color from Lyon standard color chart or by matching special color.  Consult Lyon for availability of two-tone effects and custom colors.

1.	Exterior Color:  _______________ .

Specifier Notes:  Specify interior color.

2.	Interior Color:  [Dove Gray]  [Putty]  [Match exterior color]  [ _______________ ].

PART 3	EXECUTION

3.1	EXAMINATION

A.	Examine areas to receive lockers.  Notify Architect if areas are not acceptable.  Do not begin installation until unacceptable conditions have been corrected.

3.2	INSTALLATION

A.	Install lockers in accordance with manufacturer's instructions at locations indicated on the Drawings.

B.	Install lockers plumb, level, square, rigid, with flush installation.

C.	Use manufacturer's supplied hardware.

Specifier Notes:  Lyon strongly recommends all lockers be floor and/or wall anchored to prevent tipping or injury.

D.	Anchoring:  Anchor lockers to floors and walls as indicated on the Drawings.

E.	Sloping Hoods and Metal Fillers:  Install sloping hoods and metal fillers using concealed fasteners.

F.	Joints:  Provide flush hairline joints against adjacent surfaces.

G.	Number Plates:  Attach number plates to face of doors level with 2 aluminum rivets.  Attach in sequence as indicated on the Drawings.

Specifier Notes:  Delete the following sentence if locker benches are not specified.

H.	Locker Benches:  Install locker benches by fastening bench tops to pedestals and securely anchoring to floor using appropriate anchors.

I.	Repair minor damages to finish in accordance with manufacturer's instructions and as approved by Architect.

J.	Remove and replace defective or damaged components that cannot be successfully repaired as determined by Architect.

3.3	ADJUSTING

A.	Adjust doors, locks, and operating hardware to function properly and for smooth operation without binding.

3.4	CLEANING

A.	Clean surfaces promptly after installation in accordance with manufacturer's instructions.

B.	Do not use harsh cleaning materials or methods that could damage finish.

3.5	PROTECTION

A.	Protect installed lockers from damage during construction.

END OF SECTION